PRODUCT BULLETIN

MODEL SOSM SUMP PUMPS

#### American-Marsh Model SOSM Sump Pumps are used in a variety of industries.  These rugged and efficient centrifugal pumps are designed for long life and low operational costs.  American-Marsh has been building pumps for over 130 years.  This long experience is responsible for the superior performance of the Model SOSM Sump Pumps.

Material Specifications

| PART | CONSTRUCTION |
| --- | --- |
|  | CAST STEEL CAST STEEL | CAST STEEL 316 SS | ALL 316 SS | ALL CD4MCU | ALL ALLOY 20 |
| Casing | CAST STEEL | CAST STEEL | 316 SS | CD4MCU | ALLOY 20 |
| Impeller | CAST STEEL | 316 SS | 316 SS | CD4MCU | ALLOY 20 |
| Shaft | STEEL | 316 SS | 316 SS | ZC20 | ZC20 |
| Inboard Head | CAST STEEL | CAST STEEL | 316 SS | CD4MCU | ALLOY 20 |
| Bolts, Studs & Nuts | STEEL | STEEL | 316 SS | 316 SS | 316 SS |
| Support & Discharge Pipe | STEEL | STEEL | 316 SS | 316 SS | 316 SS |

MODEL SOSM SPECIFICATIONS

Casing:  The casing is constructed of high tensile cast steel or other specified material.   It is of the volute type, carefully and accurately proportioned to permit smooth flow and to convert high velocity energy of the fluid as it leaves the impeller into pressure. Suction and discharge nozzles are flanged and are cast integral with the volute.  The casing has cast integral feet standard and the discharge port is of the vertical centerline type.  The casing assembly fully meets ANSI B73.1 dimensional requirements.  Necessary vent and drain openings can be provided upon request.

Impeller:  The impeller is of the reverse vane, end suction type, casted in one piece of cast steel or other specified material.  Running clearances need to only be adjusted between the back of the impeller and the casing adapter.  This design allows for repeatable factory tolerances, all of which can be adjusted on the bench, not just in the field.  All impellers are hydraulically and dynamically balanced prior to assembly.  Front semi-open impellers can be supplied upon request.  All models meets the stringent performance requirements of ANSI B73.1.  AMP also offers 4 Low-Flow models to meet difficult low-flow/high-head process applications.

Case Wear Ring:  Standard enclosed impellers are designed with integral case wear rings accurately turned to provide close running fits in casing.  The diameters of these rings are such as to reduce end thrust to a minimum.  On larger models a rear case wear ring is provided for additional wear resistance.

Inboard Head:  The inboard head is constructed of cast iron or other specified material.  The inboard head connects the fluid end to the support pipe and contains the inboard head bushing.

Shaft:  The shaft is of 416 stainless steel, polished and of large diameter to prevent vibration.  Lineshaft bearings are spaced to minimize shaft deflection.  The shaft is supported by the thrust bearing housing, located at the surface plate, which has integral lateral adjustment.

Support & Discharge Pipe:  The support pipe is of black iron, one end flanged to the inboard head and the other end flanges to the sump cover.  Intermediate bearings will be flanged between multiple pieces of support column and spaced accordingly.  The discharge pipe is flanged, one end connected to the discharge elbow and the other to the system piping.

Discharge Elbow:  The discharge elbow is of high tensile cast iron or of other specified material and of the long radius type flanged to the discharge of the casing and to the discharge pipe assembly.

Sump Cover:  The sump cover is of carbon steel, teardrop or of other shape as desired.  The sump cover supports the entire weight of the complete pump assembly.

SOSM Sectional Drawing

| Item Number | Item Description | Num. Req. |  | Item Number | Item Description | Num. Req. |
| --- | --- | --- | --- | --- | --- | --- |
| 1A | Casing | 1 |  | 221B | Plate, Sump Mounting | 1 |
| 2B | Head, Upper Casing | 1 |  | 224A | Flange, Upper Discharge | 1 |
| 11C | Impeller | 1 |  | 260A | Pipe, Discharge, Assembly | Varies |
| 24A | Key, Impeller | 1 |  | 280A | Pipe, Support, Assembly | Varies |
| 41A | Shaft, Pump | 1 |  | 282A | Oiler | Varies |
| 45C | Bearing, Casing Head | 1 |  | 284A | Fitting, Zerk Grease | 1 |
| 61A | Box, Stuffing | 1 |  | 301A** | Switch, Float | 1 |
| 71A | Gland, Stuffing Box | 1 |  | 302A | Bracket, Float Switch | 1 |
| 72A | Stud, Gland, with Nut | 2 |  | 303A | Rod, Float | 1 |
| 81R | Bearing, Intermediate | Varies |  | 304A | Guide, Float Rod | 1 |
| 81S | Bearing, Ball Thrust | 1 |  | 305A | Box, Float Rod Stuffing | 1 |
| 82R | Housing, Intermediate Bearing | Varies |  | 306A | Gland Nut, Float Rod Box | 1 |
| 82S | Housing, Ball Bearing | 1 |  | 307A | Stop, Float Rod | 4 |
| 85S | Cap, Bearing Housing | 1 |  | 309A | Float | 1 |
| 89S | Locknut, Ball Bearing | 1 |  | 331A | Packing, Stuffing Box | 1 set |
| 91S* | Lockwasher, Ball Bearing | 1 |  | 332A* | Packing, Float Rod Box | 1 set |
| 92S | Adapter, Ball Bearing | 1 |  | 424A | Strainer, Suction | 1 |
| 100N | Ring, Lube Seal | 1 |  | 441A | Elbow, Discharge | 1 |
| 121A | Coupling, Motor | 1 |  | 497A** | Motor | 1 |
| 122A | Coupling, Pump | 1 |  | 498A | Pedestal, Motor | 1 |
| 123A | Disc, Coupling | 1 |  | 499A | Pedestal, Extension | 1 |
| 221A | Plate, Sump Cover | 1 |  |  |  |  |

* Not Shown in sectional

** Not supplied as standard but can be ordered as an option.

Recommended spare parts are in BOLD.

# Text boxes

PRODUCT BULLETIN		MUNICIPAL				COMMERCIAL				INDUSTRIAL

MODEL SOSM SUMP		Sump, Lift Stations, Transfer,		Condensate Recovery, 	Breweries,	Spill Containment, Processing,

Filter Backwash, Supply Water		Drainage, Contact Water		Leachate Recovery, Bilge

Bulletin 320SOSM

Edition 1

Bulletin 320SOSM

Edition 1