PRODUCT BULLETIN

MODEL OSO HOT OIL

The advanced design and precision manufacture of the rugged, high temperature, heavy-duty OSO petrochemical service pump significantly enhance bearing and seal life.  American-Marsh Pumps is committed to helping users maximize mean time between planned maintenance (MTBPM).  American-Marsh Pumps’ unique features and enhancements provide significant performance benefits for pump users.  Some features of the OSO resulted from the suggestions of working engineers in the field, and were combined with others derived from the broad experience of American-Marsh engineers.  Thus practical features, backed by over 130 years of quality pump manufacturing, assure you of excellent pump performance and full satisfaction.

| PART | CONSTRUCTION |
| --- | --- |
|  | CAST STEEL CAST STEEL | CAST STEEL 316 SS | ALL 316 SS | ALL CD4MCU | ALL ALLOY 20 |
| Casing | CAST STEEL | CAST STEEL | 316 SS | CD4MCU | ALLOY 20 |
| Impeller | CAST STEEL | 316 SS | 316 SS | CD4MCU | ALLOY 20 |
| Shaft | STEEL | 316 SS | 316 SS | ZC20 | ZC20 |
| Seal Chamber | CAST STEEL | CAST STEEL | 316 SS | CD4MCU | ALLOY 20 |
| Seal Gland | ALLOY 20 | ALLOY 20 | ALLOY 20 | ALLOY 20 | ALLOY 20 |
| Power Frame | DUCTILE IRON | DUCTILE IRON | DUCTILE IRON | DUCTILE IRON | DUCTILE IRON |

Casing:  The casing is constructed of high tensile cast steel or other specified material.   It is of the volute type, carefully and accurately proportioned to permit smooth flow and to convert high velocity energy of the fluid as it leaves the impeller into pressure. Suction and discharge nozzles are flanged and are cast integral with the volute.  The casing has centerline supported feet standard and the discharge port is of the vertical centerline type.  The casing assembly nozzels fully meet ANSI B73.1 dimensional requirements.  Necessary vent and drain openings can be provided upon request.

Impeller:  The impeller is of the reverse vane, end suction type, casted in one piece of cast steel or other specified material.  Running clearances need to only be adjusted between the back of the impeller and the casing adapter.  This design allows for repeatable factory tolerances, all of which can be adjusted on the bench, not just in the field.  All impellers are hydraulically and dynamically balanced prior to assembly.  Front semi-open impellers can be supplied upon request.  All model meets the stringent performance requirements of ANSI B73.1.  AMP also offers 4 Low-Flow models to meet difficult low-flow/high-head process applications.

Shaft:  The shaft is of high strength steel or other specified material, ground to accurate dimensions and polished to a smooth surface.  It is designed for extra stiffness to avoid all critical speeds in operation.  OSO pumps lead the industry in low L3/D4 ratio’s minimizing shaft deflection at the stuffing box.  All OSO models guarantee less than 0.002” shaft deflection at the seal face location, while in operation.  As an option, the shaft can be protected by a shaft sleeve of ample thickness to ensure long life.  The shaft sleeve can be supplied in various materials.

Seal Chamber:  The seal chamber is available in five (5) different configurations depending on the jobsite requirement.  OSO pumps feature the Flow Modified (FM) seal chamber that keeps solid matter from collecting in the seal chamber causing premature seal failure.  The FM bores are available in a small bore (FMS), a large bore (FML) and a small bore with cast integral gland (FMI), all  designed to meet the process requirements of the seal industry.  OSO models can also be supplied in a standard Cyclindrical Bore (CB) arrangement.  The CB bores are available in a small bore (CBS) and large bore (CBL) both designed to meet the process requirements of the seal industry.  Seal chambers have provisions for various flush plan arrangements customizing the seal chamber to meet the requirements of the end user.  For abrasive applications, packing with a lantern ring can also be supplied.  A wide variety of component and cartridge mechanical seals can be used with OSO standard components.

Power Frame:  The power frame is constructed of high tensile ductile iron and provides support for the inboard and outboard bearings.  The outboard bearing is of the double row, angular contact type and the inboard bearing is of the single row, deep groove type for excellent axial and radial load support.  For axial adjustment of the impeller, the power frame employs a micrometer adjustment which allows the user to dial back factory tolerances between the impeller and the seal chamber.  This re-adjustment of tolerances can be done on the bench, compensating for proper seal setting and eliminating the need to have the casing near for final adjustment.  Upgraded bearing isolators ensure that contaminents are kept out of the power frame.  For extremely crucial applications, magnetic bearing isolators with a poppet breather can be specified, hermetically sealing the power frame.  The power frame has an oversized, integral oil sump that provides oil for lubrication to each bearing.  A large one inch oil level eye is provided standard on the power frame to visually indicate the oil level.  The bearings and shafts are so designed to last up to 61% longer than the competition.  With shaft deflection indicies surpassing nearly all of the competition, 43-252% greater stiffness is achieved resulting in longer Mean Time Between Planned Maintenance (MTBPM).

| Item Number | Item Description |  |  | Item Number | Item Description |  |
| --- | --- | --- | --- | --- | --- | --- |
| 100 | Casing |  |  | 124 | Bearing Locknut |  |
| 103 | Impeller |  |  | 125 | Bearing Lockwasher |  |
| 104 | Impeller Gasket |  |  | 129 | Outboard Oil Lip Seal |  |
| 105 | Shaft |  |  | 131 | Adapter O-Ring | N/A |
| 106 | Rear Cover Plate |  |  | 133 | Trico Oiler |  |
| 107 | Rear Cover Gasket |  |  | 134 | Bearing Housing Drain Plug |  |
| 108 | Bearing Housing Adapter | N/A |  | 135 | Bearing Housing Vent Plug |  |
| 109 | Bearing Housing Foot | N/A |  | 136 | Capscrew – Foot | N/A |
| 109A | Shim |  |  | 139 | Capscrew – Bearing Housing | N/A |
| 110 | Gland – Packing | OPT. |  | 140 | Capscrew – Cover/Adapter |  |
| 111 | Stud – Gland |  |  | 153 | Mechanical Seal |  |
| 111A | Hex Nut – Gland |  |  | 177 | Hook Sleeve | OPT. |
| 112 | Lantern Ring Halves | OPT. |  | 190 | Gland – Mechanical Seal |  |
| 113 | Packing | OPT. |  | 190G | Gland Gasket |  |
| 114 | Inboard Deflector | OPT. |  | 200 | Oil Sight Gage |  |
| 115 | Stud – Casing |  |  | 201 | Bearing Carrier |  |
| 115A | Hex Nut – Casing |  |  | 201A | Set Screw – Bearing Carrier |  |
| 118 | Inboard Oil Lip Seal |  |  | 201B | O-Ring – Bearing Carrier |  |
| 119 | Bearing Housing |  |  | 201C | Bearing Carrier Retainer |  |
| 120 | Inboard Bearing |  |  | 201D | Clap Ring Bearing Housing | OPT. |
| 121 | Outboard Bearing |  |  | 201E | Socket Head Capscrew Clamp | OPT. |
| 122 | Oil Slinger | OPT. |  |  |  |  |

Recommended spare parts are in BOLD.

| Item Number | Item Description |  |  | Item Number | Item Description |  |
| --- | --- | --- | --- | --- | --- | --- |
| 100 | Casing |  |  | 124 | Bearing Locknut |  |
| 103 | Impeller |  |  | 125 | Bearing Lockwasher |  |
| 104 | Impeller Gasket |  |  | 129 | Outboard Oil Lip Seal |  |
| 105 | Shaft |  |  | 131 | Adapter O-Ring |  |
| 106 | Rear Cover Plate |  |  | 133 | Trico Oiler |  |
| 107 | Rear Cover Gasket |  |  | 134 | Bearing Housing Drain Plug |  |
| 108 | Bearing Housing Adapter |  |  | 135 | Bearing Housing Vent Plug |  |
| 109 | Bearing Housing Foot | N/A |  | 136 | Capscrew – Foot | N/A |
| 109A | Shim |  |  | 139 | Capscrew – Bearing Housing | N/A |
| 110 | Gland – Packing | OPT. |  | 140 | Capscrew – Cover/Adapter |  |
| 111 | Stud – Gland |  |  | 153 | Mechanical Seal |  |
| 111A | Hex Nut – Gland |  |  | 177 | Hook Sleeve | OPT. |
| 112 | Lantern Ring Halves | OPT. |  | 190 | Gland – Mechanical Seal |  |
| 113 | Packing | OPT. |  | 190G | Gland Gasket |  |
| 114 | Inboard Deflector | OPT. |  | 200 | Oil Sight Gage |  |
| 115 | Stud – Casing |  |  | 201 | Bearing Carrier |  |
| 115A | Hex Nut – Casing |  |  | 201A | Set Screw – Bearing Carrier |  |
| 118 | Inboard Oil Lip Seal |  |  | 201B | O-Ring – Bearing Carrier |  |
| 119 | Bearing Housing |  |  | 201C | Bearing Carrier Retainer |  |
| 120 | Inboard Bearing |  |  | 201D | Clap Ring Bearing Housing | OPT. |
| 121 | Outboard Bearing |  |  | 201E | Socket Head Capscrew Clamp | OPT. |
| 122 | Oil Slinger | OPT. |  |  |  |  |

Recommended spare parts are in BOLD.

| Item Number | Item Description |  |  | Item Number | Item Description |  |
| --- | --- | --- | --- | --- | --- | --- |
| 100 | Casing |  |  | 124 | Bearing Locknut |  |
| 103 | Impeller |  |  | 125 | Bearing Lockwasher |  |
| 104 | Impeller Gasket |  |  | 129 | Outboard Oil Lip Seal |  |
| 105 | Shaft |  |  | 131 | Adapter O-Ring |  |
| 106 | Rear Cover Plate |  |  | 133 | Trico Oiler |  |
| 107 | Rear Cover Gasket |  |  | 134 | Bearing Housing Drain Plug |  |
| 108 | Bearing Housing Adapter |  |  | 135 | Bearing Housing Vent Plug |  |
| 109 | Bearing Housing Foot | N/A |  | 136 | Capscrew – Foot | N/A |
| 109A | Shim |  |  | 139 | Capscrew – Bearing Housing | N/A |
| 110 | Gland – Packing | OPT. |  | 140 | Capscrew – Cover/Adapter |  |
| 111 | Stud – Gland |  |  | 153 | Mechanical Seal |  |
| 111A | Hex Nut – Gland |  |  | 177 | Hook Sleeve | OPT. |
| 112 | Lantern Ring Halves | OPT. |  | 190 | Gland – Mechanical Seal |  |
| 113 | Packing | OPT. |  | 190G | Gland Gasket |  |
| 114 | Inboard Deflector | OPT. |  | 200 | Oil Sight Gage |  |
| 115 | Stud – Casing |  |  | 201 | Bearing Carrier |  |
| 115A | Hex Nut – Casing |  |  | 201A | Set Screw – Bearing Carrier |  |
| 118 | Inboard Oil Lip Seal |  |  | 201B | O-Ring – Bearing Carrier |  |
| 119 | Bearing Housing |  |  | 201C | Bearing Carrier Retainer |  |
| 120 | Inboard Bearing |  |  | 201D | Clap Ring Bearing Housing |  |
| 121 | Outboard Bearing |  |  | 201E | Socket Head Capscrew Clamp |  |
| 122 | Oil Slinger | OPT. |  |  |  |  |

Recommended spare parts are in BOLD.

# Text boxes

PRODUCT BULLETIN			COMMERCIAL			INDUSTRIAL

MODEL OSO HOT OIL		Boiler Feed, Transfer,		Propane, Butane, Crude Oil, Acids, Gasoline, Naphtha, Organic,

Condensate Return		Petrochemical, Black Liquor, Ammonia, Organic Fluids, Cargo Transfer