PRODUCT BULLETIN

MODEL NOVO DIAPHRAGM PUMP

##### NOVO

On the job dependability and efficiency are built into every NOVO Diaphragm Pump . . . assuring long life and top performance under the most rugged operating conditions.

The sturdy cast iron construction throughout the entire unit, simplicity of design, minimum of maintenance and low cost of replacement parts have made NOVO the choice of construction and industrial companies – both large and small.

The American-Marsh NOVO Diaphragm Pump, in your possession, offers the latest development and construction in diaphragm pumps.  Give it the same care and attention you would any piece of high grade equipment.  In turn this pump will reward you with years of dependable, satisfactory service.

Pump and power unit are mounted on a substantial, rigid steel frame and are not dependent on a foundation to maintain correct alignment between pump and driver.  The unit should set level for even wear of moving parts and for proper lubrication.

Set the pump as near the source of supply as possible.  The shorter the suction line the better; it should never exceed 25 feet vertical lift, nor a total head, suction and discharge in excess of 50 feet.  Both the suction and discharge lines should be anchored and supported independent of the pump to avoid possible misalignment and undue strain on the pump and driving parts.

INDUSTRIAL USES FOR NOVO DIAPHRAGM PUMPS

NOVO’s versatility allow them to perform a variety of jobs for industrial firms.  Most any liquid can be pumped with a NOVO including abrasive and corosive fluids.  Vital pumping parts are made with either cast iron, stainless steel, bronze or aluminum.  Diaphragms are available in rubber, plastic or a combination of the two.  The NOVO diaphragm pump is self-priming, self-lubricating, void of close clearances…handles any percentage of air and pumps at any desired rate of flow within the range of the power source.

NOVO AD Diaphragm Self-Primer Sectional Drawing

| Item Number | Item Description | AD-3-1 | AD-4-1 | AD-3-2 | AD-4-2 | AD-3-B | AD-4-B |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. |
| C108 | Crankshaft Oil Seal | 2J227 | 1 | 2J227 | 1 | 2J227 | 1 | 2J227 | 1 | 1C108 | 1 | 1C108 | 1 |
| D1 | Pump Base | 3D1G | 1 | 4D1E | 1 | 3D1G | 2 | 4D1E | 2 | 3D1G | 1 | 4D1E | 1 |
| D2 | Pump Top | 3D2C | 1 | 4D2F | 1 | 3D2C | 2 | 4D2F | 2 | 3D2C | 1 | 4D2F | 1 |
| D4 | Plunger Bottom | 3D4D | 1 | 3D4E | 1 | 3D4D | 2 | 3D4E | 2 | 3D4D | 1 | 3D4E | 1 |
| D5 | Cross Head | 3D5J | 1 | 3D5K | 1 | 3D5J | 2 | 3D5K | 2 | 3D5J | 1 | 3D5K | 1 |
| D6 | Crosshead Plate Screws | 3D6 | 6 | 4D6 | 6 | 3D6 | 12 | 4D6 | 12 | 3D6 | 6 | 4D6 | 6 |
| D9 | Suction Flange | 3D9N | 1 | 4D9B | 1 | 3D9H | 2 | 4D9D | 2 | 3D9N | 1 | 4D9B | 1 |
| D9A | Discharge Flange | 3D9L | 1 | 4D9E | 1 | 3D9L | 2 | 4D9E | 2 | 3D9L | 1 | 4D9E | 1 |
| D10 | Valve Weight (Large) | 3D10B | 2 | 4D10A | 2 | 3D10B | 4 | 4D10A | 4 | 3D10B | 2 | 4D10A | 2 |
| D12 | Valve Rubber Retainer | 3D12B | 2 | 4D12 | 2 | 3D12B | 4 | 4D12 | 4 | 3D12B | 2 | 4D12 | 2 |
| D13 | ½” Closed End Nut | 3D13A | 2 | 3D13A | 2 | 3D13A | 4 | 3D13A | 4 | 3D13A | 2 | 3D13A | 2 |
| D14 | Cap Screw (Long) | 3D14 | 5 | 3D14 | 12 | 3D14 | 6 | 3D14 | 16 | 3D14 | 5 | 3D14 | 12 |
| D14A | Cap Screw (Short) | 3D14C | 1 |  | 3D14C | 4 |  | 3D14C | 1 |  |
| D14B | Cap Screw | 3D14B | 4 | 4D14A | 4 | 3D14B | 8 | 4D14A | 8 | 3D14B | 4 | 4D14A | 4 |
| D15 | Valve Retainer Set Screw | 3D15 | 2 | 4D15 | 2 | 3D15 | 4 | 4D15 | 4 | 3D15 | 2 | 4D15 | 2 |
| D16 | Valve Weight Set Screw | 3D16 | 2 | 4D16 | 2 | 3D16 | 4 | 4D16 | 4 | 3D16 | 2 | 4D16 | 2 |
| D20 | Diaphragm | 3D20 | 1 | 4D20 | 1 | 3D20 | 2 | 4D20 | 2 | 3D20 | 1 | 4D20 | 1 |
| D22 | Check Valve | 3D22C | 2 | 4D22 | 2 | 3D22C | 4 | 4D22 | 4 | 3D22C | 2 | 4D22 | 2 |
| D23 | Suction Flange Gasket | 3D23C | 2 | 4D23E | 2 | 3D23C | 6 | 4D23E | 6 | 3D23C | 2 | 4D23E | 2 |
| D23A | Discharge Flange Gasket | 3D23D | 1 | 4D23D | 1 | 3D23D | 2 | 4D23D | 2 | 3D23D | 1 | 4D23D | 1 |
| D24 | Washer – Plain | 4D24 | 2 | 4D24 | 2 | 4D24 | 4 | 4D24 | 4 | 4D24 | 2 | 4D24 | 2 |
| D25 | Washer – Plain | 3D25 | 6 | 3D25 | 16 | 3D25 | 14 | 3D25 | 24 | 3D25 | 6 | 3D25 | 16 |
| D25A | Washer – Plain | 3D25A | 4 |  | 3D25A | 8 |  | 3D25A | 4 |  |
| D53 | Handle | 3D53 | 2 | 3D53 | 2 | 3D53 | 4 | 3D53 | 4 | 3D53 | 2 | 3D53 | 2 |
| *D55 | Stud |  | 3D55 | 2 |  |
| DH360 | Clean Out Plate Stud | DH360 | 2 | DH360 | 2 | DH360 | 4 | DH360 | 8 | DH360 | 2 | DH360 | 2 |
| J5 | Engine Pinion | 2J5U | 1 | 2J5U | 1 | 2J5U | 1 | 2J5U | 1 | 3J5F | 1 | 3J5F | 1 |
| J6 | Engine Pinion Key | 2J6 | 1 | 2J6 | 1 | 2J6 | 1 | 2J6 | 1 | 2J6 | 1 | 2J6 | 1 |
| J16 | 17 Tooth Pinion | 2J16D | 1 | 2J16D | 1 | 2J16D | 1 | 2J16D | 1 | 2J16D | 1 | 2J16D | 1 |
|  | Before Serial Number P-33306 Use 2J16C |  |
| J19 | Eccentric | 2J19T | 1 | 2J19V | 1 | 2J19T | 2 | 2J19U | 2 | 2J19T | 1 | 2J19U | 1 |
| J20 | Eccentric Key | 2J20 | 1 | 2J20 | 1 | 2J20 | 2 | 2J20 | 2 | 2J20 | 1 | 2J20 | 1 |
| J23 | Brace Nuts | 2J23 | 2 | 2J23 | 2 | 2J23 | 4 | 2J23 | 4 | 2J23 | 2 | 2J23 | 2 |
| *J23A | Suction Manifold |  | 3J23A | 1 | 4J23C | 1 |  |
| J24 | Brace Nuts | 2J24 | 2 | 2J24 | 2 | 2J24 | 4 | 2J24 | 4 | 2J24 | 2 | 2J24 | 2 |
| J25 | Pump & Jack Brace | 2J25L | 2 | 2J25L | 2 | 2J25L | 4 | 2J25L | 4 | 2J25L | 2 | 2J25L | 2 |
| J27 | 70 Tooth Int. Gear | 2J27G | 1 | 2J27G | 1 | 2J27G | 1 | 2J27G | 1 | 2J27G | 1 | 2J27G | 1 |
| J27C | 85 Tooth Gear | 2J27H | 1 | 2J27H | 1 | 2J27H | 1 | 2J27H | 1 | 2J27H | 1 | 2J27H | 1 |
|  | Before Serial Number P-33306 Use 2J27F |  |
| J29 | Int. Shaft Bushing | 2J29C | 2 | 2J29C | 1 | 2J29C | 2 | 2J29C | 2 | 2J29C | 2 | 2J29C | 2 |
| J31 | Int. Shaft | 2J31G | 1 | 2J31G | 1 | 2J31G | 1 | 2J31G | 1 | 2J31G | 1 | 2J31G | 1 |
| J42 | Plunger Bottom Stud | 2J42 | 2 | 2J42 | 2 | 2J42 | 4 | 2J42 | 4 | 2J42 | 2 | 2J42 | 2 |
| J54 | Gear Case Cover | 4J54G | 1 | 4J54G | 1 | 4J54J | 1 | 4J54J | 1 | 4J54G | 1 | 4J54G | 1 |
| J59 | Gear Case | 4J59J | 1 | 4J59J | 1 | 4J59J | 1 | 4J59J | 1 | 4J59J | 1 | 4J59J | 1 |
| J60 | Eccentric Shaft Support | 2J60B | 1 | 2J60B | 1 | 2J60B | 2 | 2J60B | 2 | 2J60B | 1 | 2J60B | 1 |
| J62 | Eccentric Support Bolts | 2J62 | 4 | 2J62 | 4 | 2J62 | 4 | 2J62 | 4 | 2J62 | 4 | 2J62 | 4 |
| J63 | Zerk Fitting | 2J63 | 3 | 2J63 | 3 | 2J63 | 4 | 2J63 | 4 | 2J63 | 3 | 2J63 | 3 |
| J74 | Eccentric Bushing | 2J74D | 2 | 2J74D | 2 | 2J74D | 4 | 2J74D | 4 | 2J74D | 2 | 2J74D | 2 |
| J76 | Eccentric Shaft | 2J76Q | 1 | 2J76Q | 1 | 2J76R | 1 | 2J76S | 1 | 2J76Q | 1 | 2J76Q | 1 |
| J115 | 5/16” x 7/8” Groove Pin | X577 | 4 | X577 | 4 | X577 | 2 | X577 | 2 | X577 | 4 | X577 | 4 |
| *J127 | Crank Shaft Sleeve | 2J127B | 1 | 2J127B | 1 | 2J127B | 1 |  |
| J141 | Gear Case Gasket | 2J141C | 1 | 2J141C | 1 | 2J141C | 1 | 2J141C | 1 | 2J141C | 1 | 2J141C | 1 |
| J140 | Ecc. Shaft Brg. Gasket | 2J140 | 1 | 2J140 | 1 | 2J140 | 1 | 2J140 | 1 | 2J140 | 1 | 2J140 | 1 |
| *J150 | Int. Shaft Thrust Washer | 1J150B | Var. | 1J150B | Var. | 1J150B | Var. | 1J150B | Var. | 1J150B | Var. | 1J150B | Var. |
| *J151 | Thrust Washer | 1J151C | 1 | 1J151C | 1 | 1J151C | 2 | 1J151C | 2 | 1J151C | 1 | 1J151C | 1 |
| J154 | Bush. For Ecc. Support | 2J154 | 2 | 2J154 | 2 | 2J154 | 4 | 2J154 | 4 | 2J154 | 2 | 2J154 | 2 |
| J157 | Oil Fill Plug | 2J157 | 1 | 2J157 | 1 | 2J157 | 1 | 2J157 | 1 | 2J157 | 1 | 2J157 | 1 |
| J158 | Oil Drain Plug | 2J158 | 1 | 2J158 | 1 | 2J158 | 1 | 2J158 | 1 | 2J158 | 1 | 2J158 | 1 |
| J170 | Adapter Capscrews | 2J170 | 3 | 2J170 | 3 | 2J170 | 3 | 2J170 | 3 |  |
| J171 | Gear Cover Capscrews | 2J171 | 11 | 2J171 | 11 | 2J171 | 11 | 2J171 | 11 | 2J171 | 11 | 2J171 | 11 |
| J172 | Motor Capscrews | 2J172 | 8 | 2J172 | 8 | 2J172 | 8 | 2J172 | 8 |  |
| J173 | Capscrew | 2J173 | 1 | 2J173 | 1 | 2J173 | 1 | 2J173 | 1 | 2J173 | 1 | 2J173 | 1 |
| J174 | Drain Cock | 2J174 | 1 | 2J174 | 1 | 2J174 | 1 | 2J174 | 1 | 2J174 | 1 | 2J174 | 1 |

*Not shown in sectional.

Recommended spare parts are in BOLD.

NOVO AD Diaphragm Self-Primer Sectional Drawing

| Item Number | Item Description | AD-3-1 | AD-4-1 | AD-3-2 | AD-4-2 | AD-3-B | AD-4-B |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. | Symbol | Qty. |
| J175 | Setscrew | 2J175 | 1 | 2J175 | 1 | 2J175 | 1 | 2J175 | 1 | 2J175 | 1 | 2J175 | 1 |
| J205 | Cross Head Side Plate | 2J205A | 2 | 2J205A | 2 | 2J205A | 4 | 2J205A | 4 | 2J205A | 2 | 2J205A | 2 |
| J222 | Side Plate Gasket | 2J222 | 2 | 2J222 | 2 | 2J222 | 4 | 2J222 | 4 | 2J222 | 2 | 2J222 | 2 |
| J223 | Hoisting Sling | EF598 | 1 | EF598 | 1 | A4443 | 1 | A4446 | 1 | EF598 | 1 | EF598 | 1 |
| *J224 | Dowel Pin | 2J224 | 2 | 2J224 | 2 | 2J224 | 2 | 2J224 | 2 | 2J224 | 1 | 2J224 | 2 |
| *J228 | Support Bracket | 4J228 | 1 | 4J228 | 1 |  |
| *J231 | Governor Stop | 4J231 | 1 | 4J231 | 1 |  |
| P158 | Clean Out Plate | 3P158A | 1 | 3P158A | 1 | 3P158A | 2 | 3P158A | 2 | 3P158A | 1 | 3P158A | 1 |
| P159 | Clean Out Plate Gasket | 3P159A | 1 | 3P159A | 1 | 3P159A | 2 | 3P159A | 2 | 3P159A | 1 | 3P159A | 1 |
| P162 | Valve Weight (Small) | 3P162B | 1 | 4D11A | 2 | 3P162B | 4 | 4D11A | 4 | 3P162B | 2 | 4D11A | 2 |
| P172 | Valve Nut | 3P172 | 4 | 3P172 | 4 | 3P172 | 8 | 3P172 | 8 | 3P172 | 4 | 3P172 | 4 |
| P173 | Discharge Flange | 3P173B | 1 | 4P173 | 1 | 3P173D | 1 | 4P173B | 1 | 3P173B | 1 | 4P173 | 1 |
| P175 | Suction Plug | 3P175 | 1 | 3P175 | 1 | 3P175 | 2 | 3P175 | 2 | 3P175 | 1 | 3P175 | 1 |
| P176 | Discharge Plug | 3P176 | 1 | 3P176 | 1 | 3P176 | 2 | 3P176 | 2 | 3P176 | 1 | 3P176 | 1 |
| V11 | Valve Spacer | 3V11 | 8 | 3V11 | 8 | 3V11 | 16 | 3V11 | 16 | 3V11 | 8 | 3V11 | 8 |
| V2 | Adapter | 2J2 | 1 | 2J2 | 1 | 2J2 | 1 | 4J2A | 1 |  |
| *V63 | Pinion Nut |  | 1V63 | 1 | 1V63 | 1 |
| *SPC22 | Shaft Seal – Outer |  | 2SPC22 | 1 | 2SPC22 | 1 |
| *SPC22A | Shaft Seal – Inner |  | 2SPC22A | 1 | 2SPC22A | 1 |
| SPC24 | Shaft |  | 2SPC24 | 1 | 2SPC24 | 1 |
| *SPC28 | Bearing Retainer |  | 2SPC28 | 1 | 2SPC28 | 1 |
| *SPC29 | Retainer Shim |  | 2SPC29 |  | 2SPC29 |  |
| SPC39 | Shaft Bearing (Outer) |  | 2SPC39 | 1 | 2SPC39 | 1 |
| SPC40 | Shaft Bearing (Inner) |  | 2SPC40 | 1 | 2SPC40 | 1 |
| *SPC92 | Oil Filler |  | 1SPC92 | 1 | 1SPC92 | 1 |
| SPC97 | Base Assembly | B2487 | 1 | B2517 | 1 | B2503 | 1 | B2515 | 1 | A4434 | 1 | B2480 | 1 |
| *U1318 | Soft Washer |  | NNU1318 | 4 |  |
| Wheeled Truck Assembly |  |
| *SPC95 | Tongue Chain Assy. | 2SPC95 | 1 | 2SPC95 | 1 |  |
| *SPC97 | Prop Assembly | 2SPC97 | 1 | 2SPC97B | 1 | 4TR182N | 1 | 4TR182N | 1 |  |
| *SPC98 | Tongue Assembly | 2SPC98 | 1 | 2SPC98 | 1 | 4TR111E | 1 | 4TR111E | 1 |  |
| *SPC99 | Axle | 2SPC99 | 1 | 2SPC99A | 1 | 4TR107X | 1 | 4TR107W | 1 |  |
| SPC102 | Handle | 2SPC102 | 1 | 2SPC102 | 1 | 2SPC102 | 1 | 2SPC102 | 1 | 2SPC102 | 1 | 2SPC102 | 1 |
| SPC104 | Motor Capscrew | 2SPC104 | 4 | 2SPC104 | 4 | 2SPC104 | 4 | 2SPC104 | 4 | 2SPC104 | 4 | 2SPC104 | 4 |
| SPC105 | Motor Nut | 2SPC105 | 4 | 2SPC105 | 4 | 2SPC105 | 4 | 2SPC105 | 4 | 2SPC105 | 4 | 2SPC105 | 4 |
| SPC106 | Motor Washer | 2SPC106 | 4 | 2SPC106 | 4 | 2SPC106 | 4 | 2SPC106 | 4 | 2SPC106 | 4 | 2SPC106 | 4 |
| SPC107 | Gear Housing Capscrew | 2SPC107 | 2 | 2SPC107 | 2 | 2SPC107 | 2 | 2SPC107 | 2 | 2SPC107 | 2 | 2SPC107 | 2 |
| SPC108 | Gear Housing Nut | 2SPC108 | 2 | 2SPC108 | 2 | 2SPC108 | 2 | 2SPC108 | 2 | 2SPC108 | 2 | 2SPC108 | 2 |
| SPC109 | Gear Housing Washer | 2SPC109 | 2 | 2SPC109 | 2 | 2SPC109 | 2 | 2SPC109 | 2 | 2SPC109 | 2 | 2SPC109 | 2 |
| SPC110 | Pump Capscrew | 2SPC110 | 4 | 2SPC110 | 4 | 2SPC110 | 4 | 2SPC110 | 4 | 2SPC110 | 4 | 2SPC110 | 4 |
| SPC111 | Pump Nut | 2SPC111 | 4 | 2SPC111 | 4 | 2SPC111 | 4 | 2SPC111 | 4 | 2SPC111 | 4 | 2SPC111 | 4 |
| SPC112 | Pump Washer | 2SPC112 | 4 | 2SPC112 | 4 | 2SPC112 | 4 | 2SPC112 | 4 | 2SPC112 | 4 | 2SPC112 | 4 |
| SPC113 | Handle Capscrew | 2SPC113 | 2 | 2SPC113 | 2 | 2SPC113 | 2 | 2SPC113 | 2 | 2SPC113 | 2 | 2SPC113 | 2 |
| SPC114 | Handle Nut | 2SPC114 | 2 | 2SPC114 | 2 | 2SPC114 | 2 | 2SPC114 | 2 | 2SPC114 | 2 | 2SPC114 | 2 |
| SPC115 | Handle Washer | 2SPC115 | 2 | 2SPC115 | 2 | 2SPC115 | 2 | 2SPC115 | 2 | 2SPC115 | 2 | 2SPC115 | 2 |
| *TR1 | Steel Wheel | 3TR1S | 2 | 3TR1S | 2 | 4TR1L | 2 | 4TR1L | 2 | 3TR1S | 2 | 3TR1S | 2 |
| *TR15 | Axle Washer | 3TR15D | 4 | 3TR15D | 4 | TR15 | 4 | TR15 | 4 | 3TR15D | 4 | 3TR15D | 4 |
| TR16 | Cotter Pin | 3TR16 | 2 | 3TR16 | 2 | 3TR16 | 2 | 3TR16 | 2 | 3TR16 | 2 | 3TR16 | 2 |

*Not shown in sectional.

Recommended spare parts are in BOLD.

# Text boxes

PRODUCT BULLETIN			MUNICIPAL				COMMERCIAL			INDUSTRIAL

MODEL NOVO DIAPHRAGM PUMP	Transfer, De-Watering, Transfer		De-Watering, Slurry, Transfer		Spill Containment, Transfer

- Your Local Authorized Distributor -

Pumps...and Pumps Only...Since 1873

Bulletin NOVOAD

Edition 4

Foot Valve with Strainer

Foot valve with strainer attached to end of suction line is recommended, particularly on long lifts.  It permits quick starting of the pump by holding water in the suction line during priming period.  The strainer prevents large pieces of trash from clogging the pump or suction and discharge lines.  Trash could also get under the check valves and hold them open. The strainer should have a good liberal area; four to six times the area of the suction opening of the pump.

NOTE:  When operating during freezing temperatures, provisions must be made to drain both the suction and discharge lines.

### Lubrication

Four points of lubrication maintenance on the pump and pear case; the eccentric (J19), the eccentric shaft (J76), the intermediate shaft (J31) and gear case (J59).  Parts J19, J76 and J31 are lubricated by zerk fittings.  They should have daily attention using a good grade of Lithium grease.  The gear case (J59) is sealed oil tight for the gears to run in a bath of oil.  Pour in one pint of medium gear oil or heavy engine oil No. 50 through filler hole in top of case.  Check oil weekly and replenish when necessary.  On older models without oil seal around main drive shaft, gears should be lubricated once or twice a day through hole in top of gear case with heavy engine oil or medium gear oil.  Ample lubrication with clean grease and oil prolongs to be had from any machine.

Sales & Marketing:  185 Progress Road ( Collierville, Tennessee ( 38017

Manufacturing:  185 Progress Road ( Collierville, Tennessee ( 38017

Phone:  (800) 888-7167

Fax:  (901) 860-2323

Clean Out

A convenient clean out plate is located directly below the discharge flange.  This provides for cleaning out of any residue that may accumulate in the pump base and for inspection of the check valves.  The clean out plate is provided with easy-off handles requiring no wrench for removal of plate.

Valves

Both suction and discharge valves are contained in accessible cages making inspection and replacement an easy matter.  Valves should be checked occasionally and replaced when worn to the extent they are not seating properly.  The length of service depends largely on the solid content of the water being pumped and how abrasive or cutting it is.

the crosshead to the plunger bottom casting (D4).  Swing the top (D2) over the crosshead.  Remove the old diaphragm and insert the new one in place, bolting the diaphragm between the crosshead and the plunger bottom.

Diaphragm

Rightfully called “The Heart of the Pump.”  For this reason your pump comes equipped with a NOVO live rubber diaphragm, which under ordinary pumping conditions will stand up many times longer than an ordinary stock diaphragm.  We strongly recommend obtaining your replacement diaphragms through your local authorized American-Marsh distributor.

The pump is designed to make replacement of the diaphragm an easy job.  Simply remove the four bolts holding the pump top (D2) and the two nuts (D13), which clamp

Air Chamber

When the pump is installed with a long suction line, an air chamber placed close to the pump in the suction line will relieve the strain on the pump and smooth up the operation.  Likewise if a long discharge line is used.

The most difficult de-watering conditions won’t keep you from getting top performance from a NOVO Single Diaphragm Pump.  Even sticks, stones, sludge or other abrasive materials won’t clog or prevent NOVO’s efficient operation.  They’re handled with ease when a NOVO’s in action.  Hundreds of difficult de-watering problems are quickly solved on public utilities, construction and maintenance projects with a 3” or 4” positive displacement model.  Select from various power units to meet your specific needs:  gasoline, diesel … either air or water cooled … or electric.

Pump & Model #			AD-3W1	AD-4W1

Pump Size			3 Inch		4 Inch

Capacities

@ 5’ Suction Lift		4,200 GPH	7,200 GPH

@10’ Suction Lift	3,900 GPH	6,900 GPH

@15’ Suction Lift	3,600 GPH	6,300 GPH

@20’ Suction Lift	3,300 GPH	5,100 GPH

@25’ Suction Lift	3,000 GPH	4,800 GPH

Weights

Skid Mounted			485 lbs.		565 lbs.

Low Speed Trailer		515 lbs.		625 lbs.

High Speed Trailer		695 lbs.		773 lbs.

Pump more water, faster, on “tough” de-watering jobs with a NOVO Double Diaphragm Pump.  One diaphragm pumps while the other discharges to give a full, steady flow.  Double Diaphragm positive displacement models are just as reliable and rugged as the single diaphragm models.  And when the NOVO goes through its paces, it handles sticks, stones, sludge and other abrasive materials with ease.  Never a problem. Select from various power units to meet your specific needs:  gasoline, diesel … either air or water cooled … or electric, in a broad range of horsepower.

Pump & Model #			AD-3W2	AD-4W2

Pump Size			3 Inch		4 Inch

Capacities

@ 5’ Suction Lift		8,400 GPH	14,400 GPH

@10’ Suction Lift	7,800 GPH	13,800 GPH

@15’ Suction Lift	7,200 GPH	12,600 GPH

@20’ Suction Lift	6,900 GPH	12,000 GPH

@25’ Suction Lift	6,600 GPH	10,500 GPH

Weights

Skid Mounted			710 lbs.		862 lbs.

Low Speed Trailer		866 lbs.		965 lbs.

High Speed Trailer		918 lbs.		1070 lbs.

Pump 4,200 GPH to 7,200 GPH Versatile, Handy, 3” or 4”

NOVO SINGLE DIAPHRAGM PUMPS

Pump 8,400 GPH to 14,400 GPH Versatile, Handy, 3” or 4”

NOVO DOUBLE DIAPHRAGM PUMPS

Bulletin NOVOAD

Edition 4

Bulletin NOVOAD

Edition 4

Bulletin NOVOAD

Edition 4

PUMP FLUID END ASSEMBLY

ECCENTRIC AND ECCENTRIC SUPPORT ASSEMBLY

Bulletin NOVOAD

Edition 4

GEAR CASE ASSEMBLY (FLEX-COUPLED)

GEAR CASE ASSEMBLY (CLOSE-COUPLED)

Bulletin NOVOAD

Edition 4

WHEELED BASE ASSEMBLY

Bulletin NOVOAD

Edition 4

Bulletin NOVOAD

Edition 4